# Statement of Approved Acceptance Criteria for Trade Waste Discharge

The following table shows the concentration limits for parameters allowable for discharge into Westernport Water’s sewerage system.

The table shows the different catchments for the wastewater treatment plants.

Cowes Waste Water Treatment Plant (WWTP) covers Phillip Island and San Remo

King Road WWTP covers Corinella, Coronet Bay, Tenby Point and Pioneer Bay

Kilcunda and Dalyston townships discharge to South Gippsland Water’s Wonthaggi WWTP under an agreement

Any trade waste discharge will require an application for a trade waste agreement.

|  | Cowes WWTP | King Road WWTP | Kilcunda and Dalyston Wonthaggi WWTP |
| --- | --- | --- | --- |
| Parameter | Concentration | Units | Concentration | Units | Concentration | Units |
| Suspended Solids | 500 | mg/L | 500 | mg/L | 600 | mg/L |
| Total Dissolved Solids | 625 | mg/L | 625 | mg/L | 1000 | mg/L |
| EC | 1000 | µs/cm | 1000 | µs/cm | 1600 | µs/cm |
| Sodium Concentration | 200 | mg/L | 200 | mg/L | 200 | mg/L |
| Oil and Grease | 0 | mg/L | 0 | mg/L | 30 | mg/L |
| Colour | 300 | admi | 300 | admi | 300 | admi |
| pH | 6 to 10 |  | 6 to 10 |  | 5 to 10 |  |
| Biological Oxygen Demand | 600 | mg/L | 600 | mg/L | 600 | mg/L |
| Chemical Oxygen Demand | 1500 | mg/L | 1500 | mg/L | 1500 | mg/L |
| Total Nitrogen | 150 | mg/L | 150 | mg/L | 150 | mg/L |
| Total K | 150 | mg/L | 150 | mg/L | 150 | mg/L |
| Ammonia Nitrogen | 50 | mg/L | 50 | mg/L | 50 | mg/L |
| Total Phosphorus | 10 | mg/L | 10 | mg/L | 10 | mg/L |
| Arsenic | 0.5 | mg/L | 0.5 | mg/L | 0.5 | mg/L |
| Cyanide as CN | 5 | mg/L | 5 | mg/L | 5 | mg/L |
| Fluoride | 5 | mg/L | 5 | mg/L | 5 | mg/L |
| Formaldehyde (expressed as HCOH) | 50 | mg/L | 50 | mg/L | 50 | mg/L |
| Phenol & chemical derivatives of Phenol (as Phenol) | 100 | mg/L | 100 | mg/L | 100 | mg/L |
| Phosphorus as P | 15 | mg/L | 15 | mg/L | 15 | mg/L |
| Total Oxidised Sulphur | 100 | mg/L | 100 | mg/L | 100 | mg/L |
| Sulphide as S | 1 | mg/L | 1 | mg/L | 1 | mg/L |
| MBAS | 500 | mg/L | 500 | mg/L | 500 | mg/L |
| Aluminium | 10 | mg/L | 10 | mg/L | 10 | mg/L |
| Beryllium | 0.2 | mg/L | 0.2 | mg/L | 0.2 | mg/L |
| Boron as B | 1 | mg/L | 1 | mg/L | 1 | mg/L |
| Cadmium | 0.05 | mg/L | 0.05 | mg/L | 0.05 | mg/L |
| Chromium (Total) | 0.5 | mg/L | 0.5 | mg/L | 0.5 | mg/L |
| Cobalt | 0.5 | mg/L | 0.5 | mg/L | 0.5 | mg/L |
| Copper | 0.1 | mg/L | 0.1 | mg/L | 0.1 | mg/L |
| Iron | 10 | mg/L | 10 | mg/L | 10 | mg/L |
| Lead | 0.3 | mg/L | 0.3 | mg/L | 0.3 | mg/L |
| Manganese | 0.4 | mg/L | 0.4 | mg/L | 0.4 | mg/L |
| Mercury | 0.001 | mg/L | 0.001 | mg/L | 0.001 | mg/L |
| Molybdenum | 0.05 | mg/L | 0.05 | mg/L | 0.05 | mg/L |
| Selenium | 0.03 | mg/L | 0.03 | mg/L | 0.03 | mg/L |
| Silver | 1 | mg/L | 1 | mg/L | 1 | mg/L |
| Nickel | 0.5 | mg/L | 0.5 | mg/L | 0.5 | mg/L |
| Tin | 0.5 | mg/L | 0.5 | mg/L | 0.5 | mg/L |
| Zinc | 0.3 | mg/L | 0.3 | mg/L | 0.3 | mg/L |
| Total Heavy Metals (not including Iron) | 10 | mg/L | 10 | mg/L | 10 | mg/L |

For further information please contact Westernport Water on 1300 720 711.